## Slide 1
Machine Learning Minor-2 Project
State of charge (SoC) prediction of Car batteries
Presented by:
P V L NARASIMHA RAO (521212)
V YASWANTH REDDY(521252)
V LAVANYA (521254)
Faculty supervisor:
Dr. K Phani Krishna

## Slide 2
Table of Contents:
  Introduction
  Models Used
  Comparison Between the Models
  Input data
  Python-Code
  Conclusion
  References

## Slide 3
Introduction
State of Charge (SoC) refers to the amount of energy stored in a battery at a specific point in time, typically expressed as a percentage of the battery's total capacity. It indicates how much charge is remaining in the battery relative to its fully charged state. SoC is a critical parameter in battery management systems, especially in applications like electric vehicles (EVs), portable electronics, and renewable energy storage. Knowing the SoC allows users to monitor the battery's energy level, estimate its remaining runtime, and make informed decisions about charging and discharging to optimize performance and extend battery life.
Determining SoC accurately can be challenging because it depends on various factors such as the battery chemistry, temperature, current flow, and age of the battery and correlation between them. Different machine learning algorithms/models are used to predict the SoC in practical applications. Some of those models are discussed in this presentation.

## Slide 4
Models Used
i)Neural Network
Neural networks are a fundamental concept in machine learning inspired by the structure and function of the human brain. They consist of interconnected nodes, or neurons, organized in layers. These layers typically includes:
  Input layer
  Hidden layers
  Output layer.
Neural networks learn by adjusting the weights of connections between neurons based on input data. This process is known as training, and it involves forward propagation of data through the network followed by backward propagation of error to update the weights.
Neural networks can perform various tasks such as image recognition, sequential data like text and time series, generating new data samples. Neural networks have achieved remarkable success in diverse fields including computer vision, natural language processing, speech recognition, and more. They form the backbone of many state-of-the-art machine learning models and are continuously evolving with advancements in research and technology.

## Slide 5
Models Used
ii) Random Forest Regressor:
Random forest regression is a powerful machine learning algorithm used for both classification and regression tasks. It is an ensemble learning model that operates by constructing numerous decision trees during training, each trained on a random subset of the dataset's features and samples. At each node of the trees, a random subset of features is considered for splitting, aiding in reducing overfitting and increasing diversity among the trees. During prediction, the final output is calculated by averaging the predictions of all individual trees, resulting in a robust and stable regression model. Random forest regression is known for its scalability and effectiveness, particularly with large datasets and high-dimensional feature spaces. It's widely applied in various domains such as finance, healthcare, and environmental science due to its ability to provide accurate predictions. Hyperparameters such as the number of trees and the maximum depth of each tree can be tuned to optimize performance. Overall, random forest regression is a versatile and powerful tool for regression tasks in machine learning.

## Slide 6
Models Used
iii) XGBoost Regression:
XGBoost (Extreme Gradient Boosting) Regressor is an advanced implementation of gradient boosting, a machine learning technique that builds a predictive model by combining the predictions of multiple simpler models, typically decision trees. XGBoost enhances traditional gradient boosting by introducing several optimizations and improvements, such as parallel computing, tree pruning, and regularization techniques, to achieve better performance and scalability. It works by iteratively building decision trees, each subsequent tree focusing on the errors made by the previous ones, gradually reducing the overall prediction error. XGBoost Regressor is widely used in various domains for regression tasks due to its efficiency, accuracy, and ability to handle large datasets with high dimensionality. It offers fine-tuning options for hyperparameters to optimize model performance, making it a popular choice for predictive modeling in both academia and industry.

## Slide 7
S.No | Aspect | Neural Networks | Random Forest Regressor | XGBoost regressor
1 | Model Type | Deep learning model | Ensemble learning model | Ensemble learning model
2 | Interpretability | Often considered black-box | Relatively interpretable | Relatively interpretable
3 | Training Time | Can be computationally intensive | Efficient training, parallelizable | Efficient training, parallelizable
4 | Scalability | Moderate scalability | Moderate scalability | High scalability
5 | Handling Non-linearity | Excellent at capturing complex patterns | Can capture non-linear relationships | Can capture non-linear relationships
6 | Hyperparameter Tuning | Numerous hyperparameters requiring tuning | Fewer hyperparameters compared to neural networks | Moderate hyperparameters requiring tuning
7 | Use Cases | Complex patterns, large datasets | Moderate to large datasets, interpretability required | Moderate to large datasets, high performance required
Comparison between the Models

## Slide 8
The load data consists of 28 columns:
·Time [s]
·Velocity [km/h]
·Elevation [m]
·Motor Torque [Nm]
·Longitudinal Acceleration [m/s^2]
·Regenerative Braking Signal
·Battery Voltage [V]
·Battery Current [A]
·Battery Temperature [°C]
Input Data
·Air Con Power[kW]
·Heater Signal
·Heater Voltage
·Ambient Temperature [°C]
·Coolant Temperature Heatercore [°C]
·Requested Coolant Temperature [°C]
·Coolant Temperature Inlet [°C]
·Heat Exchanger Temperature [°C]
·Cabin Temperature Sensor [°C]
The data is taken from “Battery and Heating data in real driving cycles”

## Slide 9
Python-Code:
·Data Preprocessing.
·Feature Engineering.
·Model Building.
·Model Evaluation.
·Model and Feature Tuning.
·Model Generalization Testing.

## Slide 10
Conclusion
Predicting the State of Charge (SoC) of a battery is very essential to maintain a good health of the battery and to optimize it’s performance. Determining SoC can be challenging due to its dependency and correlation with various factors. Here in this project by using the machine learning models such as Neural Networks, Random Forest regressor, XGBoost regressor we predicted the SoC levels of a car battery. The dataset we have used to train these models is the “Battery and Heating data in real driving cycles” data containing a total of 32 data set files categorized as TripA which is the summer data and for testing a total of 38 data set files categorized as TripB which is the winter data is used. Using MAE and MSE the analysis of losses have been done. After the analysis it is inferred that the performance on winter data set is not as effective as it is with the summer data set. It is due to the additional features present in the winter data set compared to the summer data set. After further analysis of prediction with the nominal values shows that the inference works well up to SoC of about 35%. So the model does not generalize well outside of the SoC range for which it was trained. Nevertheless, above 35% the models work still well for the winter trips.

## Slide 11
References
  Data sets
  Code